## Slide 1: US Regional Power Interconnections
Challenges and Solutions
for Grid Interconnection and Network Stability
Bob Stuart
Stuart Consulting
January 19, 2022

## Slide 2: US Regional Power Interconnections
NERC – North American Reliability Corporation
  Evolution of NERC from 1965 to Present
    Phase 1 – 1965 Northeast Blackout; 1967 Electric Reliability Power Act; PURPA
    Phase 2 – Competition; Energy Policy Act of 1992; FERC Open Access Tariff – 1996 (888);
    - Aug. 14, 2003 Blackout; Development of National Standards – 2005
    Phase 3 – Energy Policy Act of 2005; Compliance monitoring and enforcement;
    - Bulk Electric System (BES) definition; Cyber Security; Grid Resiliency

## Slide 3: Regulatory Structure with NERC/FERC
NERC is Electric Reliability Organization
  NERC – developing and enforcing national standards
  NERC audits utilities and levies fines against the utilities if standards are not met
  FERC (Federal Energy Regulatory Commission) is an executive branch of the federal government and approves of all transmission tariffs on interstate transmission; It reinforces and is the legal entity behind NERC
  Electric Utilities
    – Are comprised of Investor Owned Utilities (IOUs) such as PG&E, SCE and Florida Power and light;
    - Public Utilities such as SMUD and LADWP;
    - Coops and small PUDs; and
    - large federal government agencies such as BPA, TVA, WAPA and SRP.

## Slide 4: NERC Geographic Regions
NERC is comprised of 3 Regions
  Eastern Interconnection
  Western Interconnection
  ERCOT
Eastern INT: NPCC; RF; SERC & MRO
  500,000 MW – Peak Load
Western INT: Western Electricity Coordinating Council
  170,000 MW Peak Load
Texas RE (Reliability Entity)
  60,000 MW Peak Load

## Slide 5: NERC Reliability Standards
NERC has over 100 standards comprised of the following categories;
  BAL (Balancing) This standard addresses requirements to maintain frequency and area control error (ACE).
  CIP (Cyber Infrastructure Protection)
  COM (Interpersonal Communication)
  EOP (Event Reporting)
  FAC (Facility Interconnection Requirements)
  INT (Evaluation of Interchange Transactions)
  IRO (Reliability Coordination)
  MOD (Available Transmission System Capability)
  NUC (Nuclear Plant Interface Coordination)
  PER (Operating Personnel Credentials)
  PRC (Protective Relay and Control Standards)
  TOP (Transmission Operation)
  TPL (Transmission System Planning Performance Requirements)
  VAR (Voltage and Reactive Control)

## Slide 6: NERC Reliability Standards
CIP – Establishes requirements for cyber security and potential cyber attacks
COM – Establishes requirements for interpersonal communications between balancing authorities, transmission operators, generation operators and distribution providers
FAC – Facility Interconnection requirements; Establishes generation and transmission ratings
MOD – Responsibility of transmission owners to provide documentation and awareness of the capability of their system (ATC).
PRC – System Misoperation identification and correction; Relay maintenance standards; Underfrequency and undervoltage load shedding; relay loadability
TOP – Transmission System Operation Standards
TPL – To establish transmission system planning performance requirements; performance during single and multiple contingencies.

## Slide 7: Balancing Authority Control Center Example - CAISO
Responsible for 50,000 MW control area; Controls for 3 IOUs (PG&E, SCE & SDG&E)
Manages imports of over 20,000 MW; 2 DC 1000kV lines with 8,000 MW of capacity
Massive control center similar to NASA Space center; 15 to 20 consoles with multiple dynamic screens managing over 100,000 analog and digital points
Advanced EMS (Energy Management System) with a state estimator that allows real time power flows and 1000s of contingencies to be evaluated in minutes
Dynamic Map Board, Sequence of Events Recorder, Disturbance Monitors stamped with GPS time clocks and Dynamic Training Simulator
Manned by expert staff with state of the art tools to manage an extremely large geographic area serving a population of 30 million people.

## Slide 8: Major US Blackouts and Root Causes
1965 NE Blackout: Relay loadability and situational awareness were major causes. 20 million people lost power.
December 22, 1982: Extreme weather; Poor transmission line design; RAS design; 5 million people interrupted.
August 10, 1996: Inadequate vegetation management; situational awareness; inadequate operational planning; operating procedures. 15 million people interrupted
August 14, 2003: Inadequate vegetation management; situational awareness; operational tools; 60 million people interrupted
February 14 to February 19, 2021: Extreme cold weather; common fuel source; rotating outages – 20,000 MW; Frequency down to 59.4Hz.

## Slide 9: Network Instability Events
August 10, 1996 undamped oscillations
August 14, 2003 instability

## Slide 10: Threats to the US Interconnected Power Grid
Self Inflicted
  Violations of NERC Standards
  Inadequate maintenance
  Inadquate vegetation management
  Inadequate operational planning
  Poor transmission planning
Existential Threats
  Extreme weather
  Earthquakes
  Fires
  Cyber Attacks
  Geo Magnetic Disturbances
  HEMP (High Altitude Electric Magnetic Pulses)

## Slide 11: Challenges to the US Interconnected Power Grid
Aging Infrastructure – Many transmission lines/generators are over 50 years old
Transition from Fossil Fuel Generation to Renewable, Intermittent Generation
Renewable generation is farther from load centers
Transmission needs to be upgraded to transfer power from remote generation sources
Inadequate Operating Reserve
Many older plants that supplied regulating and operating reserve are being retired
Renewable generation is as-delivered energy – 0 operating reserve
Battery Storage on a large scale is now being proposed for renewable generation interconnection
Pumped Storage Hydro is a very good option but limited resources
Compressed Air Storage is an option

## Slide 12: Contact details
stuartb@elequant.com