## Slide 1: Non-Li technologies and solar integration
Valerio De Angelis
Energy Storage Tech & Systems
Sandia National Laboratories
vdeange@sandia.gov
2021 Southern Africa Energy Storage Systems
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
SAND2021-13004 C

## Slide 2: Solar energy is available and inexpensive
Potential solar power
% of solar generation in each country

## Slide 3: Long duration storage is needed to firm solar and other sources of renewable generation
https://doi.org/10.1016/j.joule.2019.11.009

## Slide 4: Energy storage is competitive in some cases with conventional generation
Advantages of solar generation
Solar enables a distributed infrastructure
A decentralized infrastructure can be easier to operate and maintain
Source: Lazard

## Slide 5: Battery technologies take time to develop
Chart: $B/year
| 2000 | 2005 | 2010 | 2015 | 2016 | 2017 | 2018
Lead-Acid | 17.5 | 21.5 | 26 | 33 | 35 | 36 | 37
Li-ion | 4 | 5.5 | 9.5 | 26.5 | 29 | 34.5 | 39.5
Alkaline Primaries | 2.25 | 3 | 4 | 10 | 11 | 12.1 | 13.31
Others | 3.8 | 3.5 | 4 | 3.75 | 4.25 | 2.75 | 1.5
Battery manufacturing
Growing Li-ion market (EV, Portable)
Stable and mature Lead-Acid market
Established primary Alkaline market
Other battery technologies are not well developed
Supply chains take decades to develop
Source: Avicenne Energy

## Slide 6: Several options for energy storage are available
Flexible
Modular
Grid scale

## Slide 7: Lead Acid is used for UPS and for solar firming
Simple & standardized construction
Performance degrades with temperature

## Slide 8: The lead-acid industry has an established recycling infrastructure
https://batteryinnovation.org/resources/lead-battery-market-data/
Recycling centers in the US and Mexico

## Slide 9: Recycle of lead-acid batteries in imperfect by recycling of Li-ion batteries is harder
Recycling concerns are not unique to lead-acid batteries
https://www.science.org/content/article/millions-electric-cars-are-coming-what-happens-all-dead-batteries
https://www.anl.gov/manufacturing/recycling

## Slide 10: Zn-based batteries are an environmentally friendlier alternative to lead acid
Source: http://www.joshuagallaway.com/?p=265
Zn-Ni at 1C charge/discharge
Source: Design and Performance of Large Format Nickel-Zinc Batteries E. Listerud and A. Weisenstein ZAF Energy Systems
Zn-MnO2 batteries
More complex construction

## Slide 11: Zn-based batteries can replace lead-acid batteries

## Slide 12: Data for the Zn-MnO2 batteries used with converters designed for lead-acid batteries
Top: Voltage; Bottom: Current: System test for 3 days. The system ran for 3 days paired with solar: charging when the sun was available and discharging during other times
DC Voltage
DC Current
Data from www.urbanelectricpower.com

## Slide 13: Zinc-based batteries can operate under solar panels
Data from www.urbanelectricpower.com

## Slide 14: Container-based ZnMnO2 system built in India using Li-ion BMS and power converter
14
Data from www.urbanelectricpower.com

## Slide 15: Flow batteries allow decoupling of energy and power
Benefits:
Decouple energy and power
The electrolyte has a long life
Issues:
Costs remain high
Energy density is low
Many mechanical parts
Modular systems (<50kWh)
Utility scale systems

## Slide 16: Hydrogen has high energy density but no established supply chain
Benefits:
High density of the fuel
Potential for transport
Reuse of existing infrastructure
Issues:
Proton exchange membranes
Expensive catalyst
Low efficiency
NOx production
Source: Sandia Energy Storage Handbook

## Slide 17: Summary
Specifications
Solar technology is mature and inexpensive
The existing grid infrastructure will evolve
Developing countries can take advantage of new decentralized technologies
The competition for Li cells will increase as the penetration of EV’s goes up
Lead-acid and new Zn-technologies can hit low price points and be easy to manage
Other, non-modular options, like flow batteries and H2 systems are coming to market

## Slide 18: Acknowledgements
Funded by the U.S. Department of Energy, Office of Electricity, Energy Storage program. Dr. Imre Gyuk, Program Director.
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
For questions about this presentation: vdeange@sandia.gov
Contributors:
Flow batteries: Leo J. Small, Cy H. Fujimoto, Harry D. Pratt III, Travis M. Anderson, Sandia National Laboratories
Hydrogen: Alexander J. Headley (Sandia National Laboratories), Susan Schoenung (Longitude 122 West, Inc.)
Sandia Grid Energy Storage Program Manager: Babu Chalamala