## Slide 1: Palava City: A pathway to net zero energy by 2030

## Slide 4
Project Overview
Palava is a 4,500 acre (20 Sq. km) green field city
Located in Mumbai Metropolitan Region (MMR) 45 km from financial hub of South Mumbai
Planned 7 million Sq. ft. of office space and 100,000 apartments in two phases by 2025
Residential - 28,000 homes built and occupied as of November 2017,
Commercial - 650,000 Sq. Ft. of office spaces available by March 2019

## Slide 5: Palava Development Phases
Palava I
(Completed)
18,600 flats
16,500 occupied
X 3.4 people / flat
= 56,100 people
Palava II (Underway)
Focus of project and recommendations is on Palava II
NZE transition strategy is focused on Palava II
Mobility survey data used as basis for Palava II mobility strategy recommendations
80,000 flats
X 3.4 people / flat
= 272,000 people
Palava III
(Future)
We want Palava to rank among the top 50 most livable cities in the world by 2025; this is ambitious, because at the moment, no Indian city is ranked in the top 100. We will have half a million people living in Palava in 2025, with 100,000 jobs in and around the city.
- Abhishek Lodha

## Slide 6: Overview of Project Scope
Net Zero Energy
Mobility
Water Use
Energy Use and Efficiency
Renewable
Energy
Mobility demands, solutions, and infrastructure
+
Sustainability Roadmap
Water use quantity, patterns, and infrastructure
An integrated approach to sustainability design and planning
Minimize onsite energy use, and
Maximize onsite energy generation
(see next slide)
Reduce mobility related GHG emissions, increase walkability, and enhance livability:
Provided prioritized sustainability strategies in Assessment Phase
Project scope delayed as Lodha collects additional requisite background data
Shift to non-motorized-transport [NMT] commuting,
Enable electrification of mobility, and
Develop on-site RE generation to charge public and private electric vehicles

## Slide 7: Net Zero Energy Buildings and Net Zero Carbon Mobility
Framework for identifying abatement strategies and estimating progress toward NZE
Abatement Strategies
Efficient Design
  Architectural & MEP
Reduced Consumption
  Behavioral
  Mobility NMT and EV Strategies
Onsite Generation
Feasibility Analysis
LCC Analysis
EUI Targets
Design Standards
Enhanced Design Policies
Abated Energy
Grid Purchased Energy
Abated Energy
Baseline Projected Energy
Progress toward NZE Goal
Grid Purchased Energy
Residential Flats
Residential Common
Commercial – Tennant
Commercial – Common
Schools
Clubs
STP/UGT
Amenities and misc.
Retail
Mobility Energy
Commute fuel
Non-commute fuel
Mobility Fuels
Analyses

## Slide 8: Palava Phase II Pathway to becoming a Net Zero Energy City
75% energy savings potential identified for Phase II 1
Key Takeaways
Mobility is projected to account for 64% of the energy and 43% of the CO2 emissions in 2030 under BAU
Reducing commute and promoting NMT for inner-city travel has energy abatement potential of 56%; highest impact on energy and carbon emissions in the city
Buildings under BAU ~20% better than BEE average. Building loads abated by 24% through efficiency strategies (9% of city energy), will be >40% below BEE average1
Add’l building load offset by 24% with onsite PV (9% of city energy)
Remaining city-wide energy is 25% (19% from buildings and 6% from mobility)1
See Appendix for detailed calculations, See slide 11 for EUI comparison with Bureau of Energy Efficiency (BEE) benchmark EUI
Only accounting for strategies fully quantified in the Analysis Phase. Additional abatement opportunities, including natural ventilation, efficiency and massing strategies exist that were not yet fully quantified
See slide 53 – 56 for description of additional strategies that warrant further analysis to achieve higher level of abatement
Chart: Palava Phase II Net Zero Energy Pathway (Building & Mobility Sector)
| BAU Energy Use in 2030 (kWh) | Abated Energy through reduced commute, NMT and building eff. (kWh) | Onsite Generation potential in 2030 | Unabated Energy in 2030
 | 435374325.5953 | 305854915.9846 | 0
Residential | 191829024.9404 | 33619583.6291 | 75803405.0168 | 82406036.2946
Commercial | 204182385.9946 | 73505658.9581 | 29030000 | 101646727.0366
Amenities/ Others | 52683157.2474 | 0 | 4223780 | 48459377.2474
Mobility: Commute (kWh eq.) | 628365000 | 542013000 | 16323047.0251 | 70028952.9749
Mobility: Liesure (kWh eq.) | 159340000 | 151887000 | 4139177.5687 | 3313822.4313
  Mobility Footprint
  Buildings Footprint
Mobility
Amenities
Commercial
Residential

## Slide 9: Transition Strategy for Palava to be a Model NZE City by 2030
  Residential Building Passive Design1
  Insulated Concrete Forms (ICFs) (2-5 yr)
  High Solar Reflective Index (SRI) paint (0-2 yr)
  Residential Buildings Behavioral and Equipment Efficiency Programs
  Energy efficiency awareness programs (0-2 yr)
  Energy efficient appliances program (0-2 yr)
  Commercial Efficiency Strategies
  EUI reduction through efficient plant design, VFDs, improved HVAC controls & piping design (0-2 yr)
  Central Plant / District Cooling
  Central plant for Sector 2 (0-2 yr)
  District Cooling considered (2-5 yr)
  Onsite Generation - Residential PV
  Rooftop PV for 100% common area (0-2 yr)
  Vertical Mount and Overhang PV (2-5 yr)
  Onsite Generation - Amenities PV
  School rooftop PV for NZE schools (0-2 yr)
  Clubhouse rooftop PV for NZE clubs (0-2 yr)
  Onsite Generation – PV for EV Power
  MLCP rooftop PV (for EV or other captive load) (0-2 yr)
  Carport PV street level (2-5 yr)
  NMT and EV Commuting Solutions
  Enabling live-work targets, NMT network (2-5 yr)
  Inner Palava mobility NMT & EV
  Buildout of EV infrastructure (2-5 yr)
  Onsite Generation - Commercial PV 2
  Commercial rooftop PV (0-2 yr)
  4 - 15 MW PV (large scale open access plant) (2-5 yr)
Total abatement of 75%, does not account strategies not directly quantified in Analysis Phase that can bring 25% unabated energy closer to NZE, e.g. Natural Ventilation, virtual PPA’s, as well others noted in slides 53 – 56
Microgrid strategy is under evaluation for Commercial Sector, but not included here as impact on NZE not yet quantified
ICFs and SRI combined will result in abating 31% of the residential apartment energy use
2030
Roadmap
to
NZE
11%
7%
28%
8%
40%
14%
8%
3%
69%
19%
Note: City level percentages in black; sub-sector level percentages in green (i.e. Residential, Commercial, Amenities, and Mobility).
Building and Mobility energy use abatement strategies1
75% abated energy quantified; 25% or more additional abatement opportunities remain to be quantified
Commercial
Residential
Onsite Generation
Mobility
6%
3%
10%
56%

## Slide 10: Net Zero Building Energy Recommendations and Outcomes
Three Pillars of Net Zero Energy buildings set Palava on the road to being a NZE city:
Improved envelope and thermal performance to reduce loads,
Energy efficiency strategies through efficient equipment and controls, and
Onsite renewable energy generation
Commercial
Cooling load reductions
HVAC control strategies
Improved Piping design
Optimize day lighting and glare reduction
Central Plant / District cooling
Residential
Improved envelope performance
Passive Design techniques
Efficient appliances
Behavioral programs
Onsite Generation
Rooftop PV plants
Open access contracts
Ground mount PV plants
Vertical and carport PV potential
Metrics
      Building EUI is the predominant metric for building performance1
Major Recommendations
Approach
Outcomes
Energy End Use | Baseline EUI (kWh/m2/yr) | Abated EUI: EEMs only (kWh/m2/yr) | Abated EUI: EEMs + PV (kWh/m2/yr) | BEE 2 Benchmark EUI | % Difference (BAU vs BEE Avg) | % Difference (Abated EEMs Only vs BEE Avg)
Residential Flat | 32 | 25 | 18 | 44 | 28% | 42%
Residential Common Area | 15 | 15 | NZE | -- | -- | --
Commercial Buildings | 156 | 100 | 78 1 | 182 | 14% | 45%
Schools | 14 | 14 | NZE | -- | -- | --
Club House | 101 | 101 | NZE | -- | -- | --
Further reductions to EUI to 66 are possible considering case studies and super efficient chiller design. In addition, Net Zero Energy (NZE) may feasible in commercial buildings with Open Access renewable energy contracts contingent on regulatory restrictions and utility pricing
Bureau of Energy Efficiency benchmark EUI

## Slide 11: Low Carbon Mobility Recommendations and Outcomes
Major Recommendations
Approach
Outcomes
Three Pillars to Low Carbon Mobility
      Minimize long distance commuting in personal petrol vehicle
      Maximize share of non-motorized transport within Palava
      Enable electric vehicle use and adoption
Non-Motorized Transport
Electric Vehicle Readiness
      Design guidelines for increased walkability
      Design guidelines for increased cycling
      Recommendation for NMT network layout
  Residential EV adoption forecast and required charging infrastructure
  EV charging load forecast (kWh & kW)
  Charging infrastructure guidelines
  Electrical infrastructure sizing upgrade timeline
Palava can achieve 86% reduction in commuting and 95% of leisure travel GHG by shifting to non-motorized-transport [NMT] commuting, enabling electric transportation, and developing on-site PV to charge vehicles
Mobility Energy Consumption | Baseline 2030 1 [kWh/yr/person] | Abated Scenario 2030 1 [kWh/yr/person] | Percent Reduction
Mobility: Commute (kwh/person) | 2,445 | 336 | 86%
Mobility: Leisure (kwh/person) | 620 | 29 | 95%
Used these per capita numbers multiplied by a commuter population of 257,000 (from SJ report) to calculate Phase II mobility footprint
See Appendix for detailed calculations

## Slide 12
Thank you