## Slide 1
High Performance Buildings A Case Study
15th July, 2019
Damodhar Reddy Racherla

## Slide 2
High performance of building is not a destination, it’s a journey…….”
Evolution of Building Performance @ Tech M

## Slide 3: Index
Introduction
Evaluation of Building performance @ TechM
Case Study

## Slide 4: The Consumption Spread
Chart: 
| Air Conditioning | UPS | Lighting | Others
Building Power Distribution | 0.5 | 0.3 | 0.1 | 0.1

## Slide 5: Building Performance Journey of TechM
250 units consumption PAPM
Now, 175 units consumption PAPM
2003-2004
2018-2019
Sustainability development
Focus on business benefits

## Slide 6: Improvements Happened
LIGHTING
HVAC
IT LOAD

## Slide 7: The Evolution: Air Conditioners
2003-2004
Reciprocating Chillers
R 22, R 12 Refrigerants
Scroll chillers
Primary & Secondary Chilled water pumps with VFDs
2018-2019
Screw Chillers
Centrifugal Chillers
Packaged AC
FCU
VRF
VAV
VFD
HRW
Magnetic Levitation Chillers
Radiant Cooling

## Slide 8: The Evolution: IT Load
2019
2005
Server Load Optimisation
Server Rooms Consolidation
Servers Virtualisation
Star Rated Desktops
Green Data Centeres
TFT Monitors
Laptops
Cloud Based
LED Monitors
Handheld devices
Non Standardised Server rooms
CRT Monitors
Notes: held

## Slide 9: The Evolution: Lighting
Incandescent
CFL
LED
T5
FTL
IoT Based LED
Sensor Based

## Slide 10: Case studies:
HT Ring main system for a large campus.
Radiant cooling system.

## Slide 11
Tower-7
Tower-5
Tower-3
Tower-4
Tower-1
Tower-2
Tower-6
DG Bank
Chiller yard
Cafeteria
66/11 KV RING MAIN DISTRIBUTION SYSTEM
2. SCADA monitors and control. 3. Reduction in Maintenance cost. 4. Productivity and Efficiency has increased. 5. Real-time and historical data.
BUSINESS BENEFITS: 1. Existing DG Sets 15Nos - 18500 KVA ( Range 380-1500 KVA) Replaced with 5Nos - 10,000 KVA (2000KVA each).
Huge reduction in operating cost and easy in operation
66/11KV Sub-station

## Slide 12: Radiant Cooling System Schematic & Energy Saving Pattern
Schematic of Radiant System with DOAS
Schematic of Conventional Case
Energy savings for Running Case over Conventional Case

## Slide 13: Radiation Cooling System - Versions
Ceiling Cooling System
Floor Cooling System
BUSINESS BENEFITS: 1. Better Indoor Air Quality
2. Energy Savings – 30%
3. More Uniform Temperature