## Slide 1: Sustainability in Buildings and Built Environment - A Comprehensive Approach in NBC 2016: Part 11
Madhurima Madhav
Scientist
Civil Engg Department
Bureau of Indian Standards

## Slide 2: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY
Conceptualization
Planning
Selection of Building Materials
Structural Design
Construction Practices and Management
Building Services
Plumbing Services
Operation & Maintenance

## Slide 3: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Conceptualization
Location/Siting
Environment and ecological concerns of site
Landslide hazard vulnerability (IS 14496)
Seismic hazard vulnerability (IS 1893)
Potential environmental impact of building occupancy
Recycle and reuse of wastes

## Slide 4: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Planning
Orientation
Natural lighting and ventilation (SP 41)
Use of shading devices and vegetation cover
Efficient supplementary lighting and ventilation
Open spaces in and around building
Thermal insulation
External Development

## Slide 5: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Selection of Building Materials
Impact during production, haulage, construction and
deconstruction
Industrial and agricultural waste based materials
- Fly Ash (IS 3812) & fly ash based materials, Slag (IS 12089),
GGBS (IS 16714), Ultrafine GGBS (IS 16715),
Sintered Aggregates (IS 9142),
Lignocellulosic Panel Products
Plantation timber
Bamboo (IS 15912)
Renewable natural materials of low gestation period
Efficient manufacturing technologies
Aggregates from other than natural sources (IS 383)

## Slide 6: Provisions on Use of Aggregates from other than Natural Sources in IS 383:2016
Aggregate type | Slag / Waste included | Maximum utilization in |  | 
 |  | Plain Concrete | Reinforced Concrete | Lean Concrete (less than M15 grade)
1) Coarse Aggregate |  |  |  | 
i) | Iron slag coarse aggregate | 50% | 25% | 100%
ii) | Steel slag coarse aggregate | 25% | Nil | 100%
iii) | Recycled concrete coarse aggregate (See Note 1) | 25% | 20% (only upto M25 grade) | 100%
iv) | Recycled coarse aggregate | nil | Nil | 100%
2) Fine Aggregate |  |  |  | 
i) | Iron slag fine aggregate | 50% | 25% | 100%
ii) | Steel slag fine aggregate | 25% | nil | 100%
iii) | Copper slag fine aggregate | 40% | 35% | 50%
iv) | Recycled concrete fine aggregate (See Note 1) | 25% | 20% (only upto M25 grade) | 100%
v) | Bottom Ash | Nil | Nil | 25%
NOTES 1 The source concrete for recycled concrete aggregates should not be deteriorated concrete and it is desirable to source these from site being redeveloped for use in the same site. In any given structure, only one type of manufactured coarse aggregate and one type of manufactured fine aggregate shall be used. 3 The increase in density of concrete due to use of copper slag and steel slag aggregates need to be taken into consideration in the design of structures. |  |  |  | 

## Slide 7: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Structural Design
Structural safety as environmental saviour of embodied
energy
Limit State Design – exploitation of material potential
Flyash / Slag concrete
Durability (IS 456 & IS 800)
Prefabrication and systems building approach
(IS 15916, 15917)

## Slide 8: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Constructional Practices and Management (IS 15883)
Minimizing adverse environmental impact of activities.
Limiting any adverse impact within the laws/prescribed norms
and their monitoring.
Safety of environment while working with hazardous materials
and maintaining Material Safety Data Sheets.
Management of disposal of waste from construction sites.
Considering positive environmental contribution.
Mechanism to review concerns of interested parties.
Best construction management / practices.

## Slide 9: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Building Services
Lighting and ventilation
Electrical Installations
HVAC
Sound Insulation and Noise control
Lifts and Escalators
Information & Communication Enabled Installations

## Slide 10: SUSTAINABILITY ISSUES IN BUILDING ACTIVITY (Contd…)
Plumbing Services
Water Supply
Dual Water Supply Systems
Recycle and Reuse of wastes
Drainage and Sanitation
Rain Water Harvesting
Special Wastes

## Slide 11
S.No | Major Stages | Corresponding Team | Purpose
1. | Location/siting | Design team | Proper integration of various design inputs
 | Conceptualization & planning |  | 
 | Designing and detailing |  | 
2. | Construction/ execution | Project Management & Construction Management Teams | Accomplishment in accordance with designs and specifications in a stipulated time and cost framework.
3. | Maintenance and repair | Operation & Maintenance Team or Asset Management Team or Estate Management Team | Operation, maintenance and repairs to be executed with least inconvenience and without any mismatch/ damage to structure, finishings, fittings, etc.
TEAM APPROACH

## Slide 12
COMPREHENSIVE APPROACH
Deals with all aspects relating to:
Siting, Form and design;
External development and landscape;
Envelope optimization;
Selection of appropriate materials;
Water and waste management;
Building services optimization;
Constructional practices including selection of appropriate technologies;
Commissioning, operation, maintenance and building performance tracking.

## Slide 13
SITING, FORM AND DESIGN
Protection of natural resource areas like floodplains; forests; water bodies; public parks; and agricultural land.
Least disturbance to existing soil at site and hydrology and preserving top soil
Removal of existing invasive vegetation on site and ensure none such planted post completion

## Slide 14
EXTERNAL DEVELOPMENT AND LANDSCAPE
Ensure proper landscape design including:
microclimatic conditions,
barrier free external landscape,
noise reduction/mitigating practices,
pervious paving design,
avoiding heat-island effect,
preserving top soil,
rain water harvesting
Reduce environmental impacts from parking facilities
Promote mass rapid transit systems, provide for bicycle lanes and pedestrian access

## Slide 15
ENVELOPE OPTIMIZATION
Building envelope to
conserve energy substantially.
maximise daylight,
maximise natural ventilation (access to fresh air)
modulate solar heat gain and control
integrate systems for renewable and rainwater harvesting
Proper selection of components of
walls,
roof,
fenestration (openings with or without glazing),
floor,
surface finishes
screens (jalli)

## Slide 16
MATERIALS
Environmental Concerns and Human Health and Safety
depletion of non-renewable natural resources due to extraction of raw materials,
disposal of the wastes generated,
transportation of materials,
Volatile Organic Compounds (VOCs) released during manufacture or processing of certain materials,
Minimizing Green House Gas (GHG) Emission
Selection of Building Materials
Life Cycle Assessment (LCA) of Building Materials involving
Embodied energy
Resource reuse and upgradation
Recycled content
Materials compliant with clean air and clean water, etc

## Slide 17: LIFE CYCLE ASSESSMENT
Embodied Energy
Resource Reuse and Upgradation
Recycled Contents
Reusablity / Recyclability
Natural and Plentiful
Indigenous / Locally Available
Rapid Renewability
Non-Polluting / Non-Hazardous

## Slide 18
WATER AND WASTE MANAGEMENT
Integrated approach to water supply, water waste and solid waste management in
Conceptualization, planning and design stage
Construction stage
Performance during use and corrective action,

## Slide 19
BUILDING SERVICES OPTIMIZATION
Optimization of electro-mechanical services
Solar passive techniques suiting different climate zones
Key target issues to be addressed
Building orientation
Building envelope
Design assumptions and internal load assessment
Maximize efficiency
Energy efficient design of electrical installations in buildings
Minimizing losses in the power distribution system,
Reduction of losses and energy wastage in the utilization of electrical power,
Reduction of losses due to the associated power quality problems
Appropriate metering and energy monitoring facilities.

## Slide 20
NBC 2016 recommends efforts for utilizing the renewable energy available in various forms like,
Solar energy utilization
  Solar water heating systems
  Solar steam systems for cooking, laundry, etc.
  Solar assisted refrigeration/air conditioning systems
  Solar photovoltaic systems
Wind energy utilization
Waste Utilization
  Waste heat utilization
  Solid Waste Utilization
Bio-Fuels
Hydropower
Other Renewable Energy Sources
BUILDING SERVICES OPTIMIZATION

## Slide 21
NBC 2016: Part 3 ‘Development Control Rules and General Building Requirements’ covers detailed administrative provisions for solar energy utilization.
Prescribes installation of Solar Photovoltaic Power Generation System for all plots having size 500 m2 and above.
Also encourages such installations for plots smaller than 500 m2.
BUILDING SERVICES OPTIMIZATION

## Slide 22
Other provisions in this respect in Part 3 of the Code:
Installation of either solar panels on roof tops, or integrated photovoltaic panels on walls/windows, or solar photovoltaic (PV) banks on open areas.
Utilization of power so generated for either in-house or for transfer to the grid.
The Authorities to have required provisions in the building bye-laws and mechanism for required clearances and approvals.
The Authority to also specify minimum generation requirement.
The Code also provides guidance for minimum generation requirements.
BUILDING SERVICES OPTIMIZATION

## Slide 23
The Code also prescribes requirement of installation of Solar Water Heating System for the following building occupancies for supplying hot water:
Residential buildings (except hostels of educational buildings and plotted houses) having plot area 4 000 m2 and above;
Plotted houses having plot area of 250 m2 and above;
Hostels for schools, colleges and training centres for more than 100 students;
Institutional buildings; and
Assembly buildings.
BUILDING SERVICES OPTIMIZATION

## Slide 24
Other provisions in this respect in Part 3 of the Code:
The Authority shall have required provisions in the building bye-laws and mechanism for required clearances and approvals.
The Authority, considering the availability of solar energy for harnessing, shall decide the minimum capacity to be installed subject to a minimum of 25 litre per day hot water yield for each bathroom and kitchen.
BUILDING SERVICES OPTIMIZATION

## Slide 25
For solar water heating system and their installation, reference to following Indian Standards should be made:
IS 12933 Solar flat plate collector — Specification
(Part 1) : 2003 Requirements (second revision)
(Part 2) : 2003 Components (second revision)
(Part 3) : 2003 Measuring instruments (first revision)
(Part 5) : 2003 Test methods (second revision)
IS 12976 : 1990 Solar water heating systems — Code of practice
BUILDING SERVICES OPTIMIZATION

## Slide 26
NBC 2016 in its Part 9/Section 1 covers provisions relating to installation (including piping) for solar assisted water heating systems.
NBC 2016 in its Part 8/Section 2 recommends to plan buildings electrical services in a manner to integrate with alternate sources of energy such as solar energy.
The Code in its above chapter also covers provisions relating to electrical installations of Solar Photovoltaic Power Generation System. Lightning protection for buildings with roof-top solar PVs and water heating systems and large solar PV power plants/farms is also covered in this chapter of the Code.
BUILDING SERVICES OPTIMIZATION

## Slide 27
NBC 2016 in its Part 8/Section 3 ‘Building Services, Air Conditioning, Heating and Mechanical Ventilation’ covers provisions relating to utilization of solar heat energy for heating buildings.
Also, various passive heating (like solar chimneys, trombe walls, etc) and passive cooling techniques (nocturnal cooling, courtyards, etc) have been discussed in Part 11 of the Code.
NBC 2016 in its Part 11 also prescribes use of Solar Photovoltaic Systems for lighting purpose in remote non-grid areas. The use of common SPV lighting systems, a) Solar lantern, b) Fixed type solar home lighting system, and c) Street lighting system has been prescribed. Guiding provisions on their use have been provided.
BUILDING SERVICES OPTIMIZATION

## Slide 28
CONSTRUCTIONAL PRACTICES
The framework for sustainable construction practices includes the following issues:
Pre-construction pre-requisites
Planning for sustainable construction
Preparation of sustainable construction management plan
Planning, monitoring and control of environmental descriptors
Sustainable work execution procedures
Effective use of water
Construction waste management
Post-construction closeout
Construction methodology for heritage buildings
Alternative use, de-construction, dismantling, demolition.

## Slide 29
IS No. | Title | Current Stage
IS 15883 | Construction Project Management- Guidelines: | 
Part 1:2009 | Part 1 General | Published
Part 2:2013 | Part 2 Time Management | Published
Part 3:2015 | Part 3 Cost Management | Published
Part 4:2015 | Part 4 Quality Management | Published
Part 5:2013 | Part 5 Health & Safety Management | Published
Part 6:2015 | Part 6 Scope Management | Published
Part 7 | Part 7 Procurement Management | Draft prepared
Part 8:2015 | Part 8 Risk Management | Published
Part 9:2018 | Part 9 Communication Management | Published
Part 10 | Part 10 Human Resource Management | Draft prepared
Part 11 | Part 11 Sustainability Management | Draft prepared
Part 12:2016 | Part 12 Integration Management | Published
IS 16416:2016 | Guidelines for Construction Project Formulation and Appraisal | Published
IS 16601:2016 | Guidelines for Habitat and Welfare Requirements for Construction Workers | Published
CONSTRUCTION PROJECT MANAGEMENT

## Slide 30
COMMISSIONING, OPERATION, MAINTENANCE AND BUILDING PERFORMANCE TRACKING
Formation of commissioning team comprising owner, users, occupants, O&M staff, and design professionals and owners.
Project design document to include a commissioning plan.
O&M programmes to focus on improving energy efficiency of building systems.
Good maintenance practices to be implemented for substantial savings in consumption of energy and water.
Regular monitoring of the performance to be carried out which will provide information on whether the set environmental performance and targets have been met or not.
Measurement and verification (M&V) process to cover monitoring of the energy and water systems to ensure ongoing accountability of energy and water consumption during the life of building.

## Slide 31
SOME POINTS REGARDING SUSTAINABILITY
To get the maximum benefit from the building and its services in terms of quality, timely completion and cost-effectiveness. The aim is to maximize the efficiency of the total system through appropriate optimization of each of its sub-systems. In the team, the inputs from each of the professional disciplines have to be so optimized that the total system’s efficiency becomes the maximum. It may be re-emphasized that maximizing the efficiencies of each sub-system may not necessarily assure the maximization of the efficiency of the total system.

## Slide 32
NATIONAL BUILDING CODE OF INDIA 2016

## Slide 33: CONTENTS OF NBC 2016
Part No. | Title
Part 0 | Integrated Approach – Prerequisite for Applying Provisions of the code
Part 1 | Definitions
Part 2 | Administration
Part 3 | Development Control Rules and General Building Requirements
Part 4 | Fire and Life Safety
Part 5 | Building Materials
Part 6 | Structural Design
Part 7 | Constructional Management, Practices and Safety
Part 8 | Building Services
Part 9 | Plumbing Services (including Solid Waste Management)
Part 10 | Landscape Development, Signs and Outdoor Display Structures
Part 11 | Approach to Sustainability
Part 12 | Asset and Facility Management

## Slide 34: ENORMOUS NATIONAL INVOLVEMENT AND RESPONSE IN PREPARATION IMPLEMENTATION - Central Govt - State Govt - State Local Bodies - Planning Commission - Housing Finance Institutions (RBI, HUDCO, NHB) - Academic Institutions

## Slide 35: www.bis.gov.in ced@bis.gov.in Locate our Indian Standards at www.standardsbis.in
THANKS FOR YOUR KIND ATTENTION