## Slide 1: Platforms for Advanced Wireless Research One Year On: Progress, Lessons, New Investments
https://www.advancedwireless.org/
Jacques Fluet on behalf of Abhimanyu Gosain
Technical Program Director

## Slide 2: Platforms for Advanced Wireless Research
1
1
2
Industry Consortium
<$ + In-Kind>
$50M
NSF
<$>
$50M
Kick-Off April 2017

## Slide 3: Level-Setting: PAWR Approach
Attribute |  | Approach
Problem Definition |  | Enhanced efforts of ~400 university researchers who need mid-scale testing capabilities to ensure success
Early Industry Involvement |  | Multi-use research platforms with “pre-competitive” research topic areas selected bottom-up by university PIs, with industry input
Research Scope |  | Mid-sized areas within cities, experimental platforms, 10-20 antenna sites, backhaul, SDRs
Flexibility and Speed |  | 1 - 2 platforms per year in years 1 and 2
Streamlined governance, deployment, and operation |  | One governance consortium focused on upfront research and policy; city/university teams propose how to streamline deployment and ops

## Slide 4
Charter Members
PPO is Looking for more Industry Partners….

## Slide 5
PAWR Awardees
http://powderwireless.net http://cosmos-lab.org
Announced April 9 2018

## Slide 6: COSMOS: Cloud Enhanced Open Software Defined Mobile Wireless Testbed for City-Scale Deployment
Deployment Area: West Manhattan/Harlem
A multi-layered computing system with an RF thin client; flexible signal processing; network function virtualization (NFV) between a local SDR (with FPGA assist) and a remote cloud radio access network (CRAN) with massive CPU/GPU and FPGA assist
Deployed in New York City, one of the country’s most populated urban centers
Wideband radio signal processing (with bandwidths of ~500 MHz or more)
Support for mmWave communication (28 and 60 GHz)
Optical switching technology (~1µs) provides passive WDM switch fabrics and
radio over fiber interfaces for ultra-low latency connections
28GHz phased-array ICs and phased-array antenna modules (PAAM)
COSMOS Radio Site Design All-Optical Network Design

## Slide 7: COSMOS mmWave Node Specifications
• 64-dual polarized antennas and 4 ICs
each with 32 TRX elements
• 128 TRX elements in total
• 8 independent 16-element beamformers,
each supporting 1 polarization of 16 ant.
• RF true time delay based architecture
• 28GHz RF, 5GHz ext. LO, 3GHz input/output IF
• 54dBm saturated EIRP on each polarization

## Slide 8: POWDER: Platform for Open Wireless Data-driven Experimental Research
RENEW: A Reconfigurable Eco-system for Next-generation End-to-end Wireless
RENEW Massive MIMO base station
End-to-End Programmable
Diverse Spectrum Access 50 MHz-3.8GHz
Hybrid Edge computer composed of FPGA and GPU/CPU-based processing,
Hub Board aggregates/distributes streams of radio samples
Next Generation Wireless Architecture
Dynamic Spectrum Sharing
Distinct environments: a dense urban downtown and a hilly campus environment.
Control Framework with Hardware + Software Building Blocks
IRIS software-defined radio modules
Architectural view of RENEW base station
Deployment Area: UofU Campus +Downtown SLC + Connected Corridor

## Slide 9: System Architecture
Controlled RF
Fiber Fronthaul/Backhaul
Edge Compute
Metro Cloud
Remote Cloud
Wide Area
Stationary Radios
Predictable Couriers
Sensors
Backpacks
Unpredictable
Core
Edge
Radio
Access

## Slide 10: Truly City scale…
Campus Shuttle Routes
Base station locations

## Slide 11: Status as of July‘19
http://powderwireless.net
Software Profiles:
  GNU Radio
  OAI TDD
  ONAP
  MATLAB
  O-RAN
  RENEW mMIMO software
Usage statistics:
  Number of projects: 25
  Number of users: 102
  Number of experiments: 1090

## Slide 12
http://powderwireless.net
http://renew.rice.edu
POWDER-RENEW
http://cosmos-lab.org
COSMOS
http://advancedwireless.org
PAWR Project
ACKNOWLEDGEMENTS