## Slide 1
Liquid Fuels and International Standardization Efforts
Standards Alliance Workshop on Biofuel Standards for Household Cooking & Transportation
Kari Cook
Quality Manager at POET Biorefining
November 14, 2019

## Slide 2: A LITTLE ABOUT ME
BS Chemistry
MS Management and Leadership (in process)
Laboratory Work since 2001
  Air quality monitoring
  Catalyst research
Quality Manager POET Biorefining
  2008 during startup

## Slide 3: POET
In the last 30 years, grown from a single, humble refinery to the world’s largest producer of ethanol and other biorefined products.
  27 Corn processing plants
  1 Cellulosic processing plant
Products Produced:
  Biofuel
  Feed Solutions
  Asphalt Rejuvenator
  Carbon Dioxide
  Clean Cooking
Our vision is to live in a world with natural balance. Where we no longer take from the Earth, but rather use its enormous ability to regenerate. Where we are no longer dependent on fossil fuels, but rather rely on the power of nature and the genius of the human spirit. Where farmers are the creators, and innovators are the heroes. Where we use the resources given to us in ways we believe God intended.

## Slide 4: POET – The Big Picture
POET
Professional Management Consultation
Biorefining Production Base
Engineering, Design & Construction
Research & Development
Feed Ingredient Marketing & Consultation
Fuel Marketing
Grain Procurement
>1.9B Gal Annually
Transportation
Home Cooking
Industrial Grades
>500M Bu Annually

## Slide 5: POET Biorefining - Alexandria
Located in Indiana
Opened in 2008
24/7 Operations
~45 Team Members
Products Produced:
  Biofuel
    Denatured Ethanol, Ethanol Blended Fuels
  Animal Food
    DDGS, Wet Cake, Syrup, Corn Oil

## Slide 6: Quality Manager – A day in the life
Laboratory Operations – sampling, testing, certifications
Fermentation – Recipe optimization
Water Treatment – sampling and testing of boilers, cooling tower, RO
Food Quality – compliance with state and federal regulations
Fuel Quality – compliance with state, federal, and international regulations
  ASTM International Standards
    Use of standards since 2008
    Active participation since 2014

## Slide 7: Standardized Fuel Quality
Consistency is imperative for customers and consumers
ASTM International Organization for Standards
  Consensus Organization
  Membership
    Producers, automotive manufacturers, regulators, users, general interest groups
Standard Test Methods
  The HOW TO perform the analysis
  Ensure samples are tested the same way

## Slide 8: Standardized Fuel Quality
Standard Specifications
  Provide properties limits that producers MUST achieve
    If product does not meet specification
      Quality Issue
      Safety Issue
  Specs allow the blenders to know how to blend
  Specs let the customer know what they are buying
Consistency is imperative for consumers!
Standards help to achieve consistency in the marketplace.

## Slide 9: ASTM COMMITTEES
D02: Petroleum Products, Liquid Fuels, and Lubricants
  D4814 Automotive Spark Ignition Engine Fuel
  D4806 Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel
  D5798 Ethanol Fuel Blends For Flexible-Fuel Automotive Spark-Ignition Engines
E48 Bioenergy and Industrial Chemicals from Biomass
  E3050 Home Cooking Standard
  Undenatured Ethanol Specification (In Progress)

## Slide 10: ASTM SUB-COMMITTEES
Address specific segments within the general subject area of the committee
Sub-committee Designations
  Letter– Specifications
    D02.A
  Numerical – Test Methods
    E48.05
Common sub-committees
  Executive
    Strategic planning, bylaws administration
  Terminology
    Alignment of definitions of terms

## Slide 11: ASTM D02 SUB-COMMITTEES D02: Petroleum Products, Liquid Fuels, and Lubricants
D02.A0 Gasoline and Oxygenated Fuels
  D4814, D4806, D5798
DO2.03 Elemental Analysis – Sulfur, Sulfate/Chloride
D02.04 Hydrocarbon Analysis – Density, Ethanol/Methanol Content
D02.06 Analysis of Liquid Fuels and Lubricants – Acidity, Water
D02.08 Volatility – Vapor Pressure
D02.14 Stability and Cleanliness of Liquid Fuels – Corrosion, gums

## Slide 12: ASTM E48 SUB-COMMITTEES E48 Bioenergy and Industrial Chemicals from Biomass
E48.A Under development
  Will hold Specifications
E48.05 Biomass Conversion
E48.80 Sustainability of Bioenergy and Industrial Chemicals from Biomass

## Slide 13: PRODUCTS WITH STANDARDS
Denatured Ethanol
  Fuel Blending
    D4806
      Defines specifications for ethanol to be used in transportation fuel blending
  Cook Stoves
    E3050
      Defines specifications for ethanol to be used in home cooking
Undenatured Ethanol
  Industrial and Intermediary Applications
2016
NEW

## Slide 14: D4806
Property | Limit | Method
Ethanol, % by volume, min | 92.1 | D5501
Methanol, % by volume, max | 0.5 | D5501
Solvent-washed gum content, mg/100 mL, max | 5.0 | D381
Water, % by volume (% by mass), max | 1.0 (1.26) | E203, E1064, or D7923
Inorganic Chloride, mg/kg (mg/L), max | 6.7 (5) | D7319 or D7328
Copper, mg/kg, max | 0.1 | D1688
Acidity (as acetic acid CH3COOH) mg/kg, (% by mass) [mg/L], max | 70 (0.0070) [56] (Note 2) | D7795
pHe | 6.5 to 9.0 | D6423
Sulfur, mg/kg, max | 30. | D2622, D3120, D5453, or D7039
Existent sulfate, mg/kg, max | 4 | D7318, D7319, or D7328

## Slide 15: UNDENATURED ETHANOL
Problem:
  No standard existed to provide specifications for undenatured ethanol
  Product movement limited/delayed due to lack of specifications
Solution:
  Develop new ASTM Standard Specification

## Slide 16: UNDENATURED ETHANOL
Scope
  This standard covers biomass derived, undenatured ethanol intended for use in industrial applications such as adhesives, detergents, inks, chemicals, plastics, paints, thinners, etc.
Parameter | Limit | ASTM TM
Specific Gravity, 20C | Report | D4052
Ethanol, % by volume, min. | Report | D5501
Water, % by volume, max. | Report | D7923, E1064
Acidity (as acetic acid) mg/ kg (% by mass) [mg/L] | 70 (0.0070)[56] (Note 2) | D7795
Nonvolatile Residue, mg/ ml, max. | 5 | D1353
Odor | Typical | D1296
Color, Pt- Co, max. | 10 | D1209
PROPOSED

## Slide 17: SPECIFICATION DEVELOPMENT
Work Item
Define scope
Assign technical contact
Task Group
Membership
Meetings and discussions
Sub-Committee
Ballot/Voting
Negatives, comments
Sub-committee Approval
Committee
Back to Task Group
Rework
Ballot/Voting
Negatives, comments
Publication
Undenatured Specification

## Slide 18: ASTM BALLOT PROCESS
Consensus Achieved through balloting process
Voting bodies
  Affirmative, Negative, Abstain
Adjudication of negative votes
Task Group
Sub Committee
Main Committee
Work Item

## Slide 19: EXPERIENCES
Industry goals include developing export markets.
Globally, these shipments often require 3rd party labs that are unfamiliar with ethanol. Contract terms typically state adherence to D4806.
D4806 allows for use of D1613 or D7795 for acidity testing
  D1613 Test Method for Acidity in Volatile Solvents and Chemical Intermediates Used in Paint, Varnish, Lacquer, and Related Products
  D7795 Test Method of Acidity in Ethanol and Ethanol Blends by Titration
    2 methodologies: Potentiometric and Colorimetric
    Referee method
?

## Slide 20: EXPERIENCES cont.
D1613 has known interferences with dissolved CO2, which can lead to erroneously high acidity results.
Many erroneous results from labs using D1613, because it doesn’t have all of the information that D7795 contains.
This causes resampling/retesting cycle that stalls vessels, leading to demurrage and other financial penalties.
Proposed removal of D1613 from D4806

## Slide 21: EXPERIENCES cont.
Resistance to the change
  Select appropriate labs
  Specify D7795 in contracts
Mitigation of the resistance
  Some international labs not familiar with the product and interferences
  Contracts reference adherence to D4806
  D1613 was originally modified to work with ethanol and ethanol blends
    Does not include all of the information that D7795 includes
  D7795 was created and approved over 5 years prior
    Time consuming process
  D7795 allows for both methods and no additional steps or equipment required

## Slide 22: LOOKING AT MOZAMBIQUE
What can you learn from the standards process?
How can ethanol standards be useful for Mozambique?
Standards that could benefit Mozambique
  Blending denatured ethanol for fuel
    Fuel quality, consumer protection
  Denatured ethanol for cooking
    Consumer protection
  Undenatured ethanol
    International market suppliers
ASTM and E48 can help!

## Slide 23: CONTACT INFORMATION
Kari Cook, Quality Manager – POET Biorefining Alexandria
Kari.cook@poet.com
www.poet.com
THANK YOU!